## Slide 1: Gates and Logic
Hakim Weatherspoon
CS 3410, Spring 2012
Computer Science
Cornell Universty
See: P&H Appendix C.2 and C.3 (Also, see C.0 and C.1)

## Slide 2: What came was Von Neumann Architecture?
The calculator
The Bombe
The Colossus
The ENIAC
All of the above

## Slide 3: What came was Von Neumann Architecture?
Notes: All of the above
Pictures show the Bombe built by Alan Turing to break the enigma machine ciphers.
They were Fixed-Program Computers came before stored-program computers (general purpose)
The former required re-wiring (e.g. ENIAC took 3 weeks to “re-wire”).

## Slide 4: A switch
Acts as a conductor or insulator
Can be used to build amazing things…

## Slide 5: Goals for today
To understand how to program,
we will build a processor (i.e. a logic circuit)
Logic circuits
  Use P- and N-transistors to implement NAND or NOR gates
  Use NAND or NOR gates to implement the logic circuits
  Build efficient logic circuits

## Slide 6: Better Switch
One current controls another (larger) current
Static Power:
  Keeps consuming power when in the ON state
Dynamic Power:
  Jump in power consumption when switching

## Slide 7: Atoms
e
N
P
N
P
N
P
N
P
N
P
N
P
N
P
e
e
e
e
e
e
e
e
e
e
e
e
e
hole

## Slide 8: Elements
B
e
e
e
e
Si
e
e
e
Silicon
Phosphorus
Boron
e
P
e
e
e
e

## Slide 9: Silicon Crystal
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
Silicon

## Slide 10: Phosphorus Doping
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
N-Type: Silicon + Phosphorus
e
P
e
e
e
e
e
P
e
e
e
e
e
P
e
e
e
e
e
P
e
e
e
e
Notes: neutral -> conductor
high voltage -> insulator

## Slide 11: Boron Doping
B
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
P-Type: Silicon + Boron
B
e
e
e
B
e
e
e
B
e
e
e
Notes: neutral -> conductor
low voltage -> insulator

## Slide 12: Semiconductors
Insulator
n-type (Si+Phosphorus) has mobile electrons:
p-type (Si+Boron)
has mobile holes:
low voltage (mobile electrons) → conductor high voltage (depleted)
→ insulator
low voltage (depleted) → insulator high voltage (mobile holes) → conductor

## Slide 13: Bipolar Junction
P-Type
N-Type
e
e
e
e
e
e
e
e
e
e
e
e
e
e
low v → conductor high v → insulator
low v → insulator high v → conductor

## Slide 14: Reverse Bias
P-Type
N-Type
e
e
e
e
e
e
e
e
e
e
e
e
e
+
–
low v → conductor high v → insulator
low v → insulator high v → conductor
e

## Slide 15: Forward Bias
P-Type
N-Type
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
–
+
low v → conductor high v → insulator
low v → insulator high v → conductor

## Slide 16: Diodes
p-type
n-type
PN Junction “Diode”
Conventions: vdd = vcc = +1.2v = +5v = hi vss = vee = 0v = gnd

## Slide 17: PNP Junction
p-type
p-type
n-type

## Slide 18: Bipolar Junction Transistors
Solid-state switch: The most amazing invention of the 1900s
Emitter = “input”, Base = “switch”, Collector = “output”
p
n
p
C
E=vdd
B
E
C
B
vdd
p
n
vss=E
C
B
C
E
B
vss
n
PNP Transistor
NPN Transistor

## Slide 19: Field Effect Transistors
P-type FET
Connect Source to Drain when Gate = lo
Drain must be vdd, or connected to source of another P-type transistor
N-type FET
Connect Source to Drain when Gate = hi
Source must be vss, or connected to drain of another N-type transistor
Drain = vdd
Source
Gate
Drain
Source = vss
Gate

## Slide 20: Multiple Transistors
In | Out
voltage
Gate delay
transistor switching time
voltage, propagation, fanout, temperature, …
CMOS design (complementary-symmetry metal–oxide–semiconductor)
  Power consumption = dynamic + leakage
in
out
Vdd
Vss
t
0v
+5v

## Slide 21: Digital Logic
In | Out
+5v | 0v
0v | +5v
voltage
in
out
Vdd
Vss
t
0v
+5v
+2v
+0.5v
In | Out
truth table
Conventions: vdd = vcc = +1.2v = +5v = hi = true = 1 vss = vee = 0v = gnd = false = 0

## Slide 22: NOT Gate (Inverter)
In | Out
0 | 1
1 | 0
in
out
Truth table
Function: NOT
Symbol:
in
out
Vdd
Vss

## Slide 23: NAND Gate
A | B | out
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
b
a
out
A
out
Vdd
Vss
B
B
A
Vdd
Function: NAND
Symbol:

## Slide 24: NOR Gate
b
a
out
A
out
Vss
Vdd
B
B
A
Vss
Function: NOR
Symbol:
A | B | out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 25: Building Functions
AND:
OR:
NOT:

## Slide 26: Universal Gates
NAND is universal (so is NOR)
  Can implement any function with just NAND gates
    De Morgan’s laws are helpful (pushing bubbles)
  useful for manufacturing
E.g.: XOR (A, B) = A or B but not both (“exclusive or”)
Proof: ?

## Slide 27: Administrivia
Make sure you have access to CMS and Piazza.com
Lab Sections started this week
  Lab0 turned in during Section
  Bring laptop to section, if possible (not required)
  Lab1 available Monday next week (due following Monday)
  Group projects start in week 4 (partner in same section)
Homework1 available Monday
  Due following Monday
Office hours start next week
  More information available on website by this weekend
Clickers not required, bring to every lecture
  Participation, not attendance

## Slide 28: Example: Big Picture
Computer System Organization and Programming platform from 10 years ago
  P- and N-transistors -> NAND and NOR gates -> logic circuit -> processor -> software -> applications (computers, cell phones, TVs, cars, airplanes, buildings, etc).
Notes: NAND and NOR gates can implement any logic circuit
i.e. a computer processor
Use P- and N-transistors to implement NAND or NOR gates

## Slide 29: Big Picture: Abstraction
Hide complexity through simple abstractions
  Simplicity
    Box diagram represents inputs and outputs
  Complexity
    Hides underlying P- and N-transistors and atomic interactions
in
out
Vdd
Vss
in
out
out
a
d
b
a
b
d
out

## Slide 30: Logic Equations
Some notation:
constants: true = 1, false = 0
variables: a, b, out, …
operators:
  AND(a, b) = a b = a & b = a  b
OR(a, b) = a + b = a | b = a  b
NOT(a) = ā = !a = a

## Slide 31: Identities
Identities useful for manipulating logic equations
  For optimization & ease of implementation
  a + 0 =
  a + 1 =
  a + ā =
  a 0 =
  a 1 =
  a ā =
  (a + b) =
  (a b) =
  a + a b =
  a(b+c) =
  a(b+c) =
  a
  1
  1
  0
  a
  0
  a b
  a + b
  a
  ab + ac
  a + bc
Notes: Minimization activity

## Slide 32: Logic Manipulation
functions: gates ↔ truth tables ↔ equations
Example: (a+b)(a+c) = a + bc
a | b | c |  |  |  |  | 
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 
Notes: (a+b)(a+c)
= aa + ab + ac + bc
= a + a(b+c) + bc
= a(1 + (b+c)) + bc
= a + bc

## Slide 33: Logic Manipulation
functions: gates ↔ truth tables ↔ equations
Example: (a+b)(a+c) = a + bc
a | b | c |  |  |  |  | 
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 
 |  |  | a+b | a+c | LHS |  | 
 |  |  | 0 | 0 | 0 |  | 
 |  |  | 0 | 1 | 0 |  | 
 |  |  | 1 | 0 | 0 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  |  |  |  | bc | RHS
 |  |  |  |  |  | 0 | 0
 |  |  |  |  |  | 0 | 0
 |  |  |  |  |  | 0 | 0
 |  |  |  |  |  | 1 | 1
 |  |  |  |  |  | 0 | 1
 |  |  |  |  |  | 0 | 1
 |  |  |  |  |  | 0 | 1
 |  |  |  |  |  | 1 | 1
Notes: (a+b)(a+c)
= aa + ab + ac + bc
= a + a(b+c) + bc
= a(1 + (b+c)) + bc
= a + bc

## Slide 34
Notes: Think-Pair-Share: Why does minimization matter

## Slide 35: Predictive – logic minimization
How to standardize minimizing logic circuits?

## Slide 36: Logic Minimization
A common problem is how to implement a desired function most efficiently
One can derive the equation from the truth table
How does one find the most efficient equation?
  Manipulate algebraically until satisfied
  Use Karnaugh maps (or K maps)
a | b | c | minterm
0 | 0 | 0 | abc
0 | 0 | 1 | abc
0 | 1 | 0 | abc
0 | 1 | 1 | abc
1 | 0 | 0 | abc
1 | 0 | 1 | abc
1 | 1 | 0 | abc
1 | 1 | 1 | abc
for all outputs
that are 1,
take the corresponding minterm
Obtain the result in
“sum of products” form

## Slide 37: Karnaugh maps
Encoding of the truth table where adjacent cells differ in only one bit
a | b | out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
truth table for AND
Corresponding Karnaugh map
ab

## Slide 38: Bigger Karnaugh Maps
3-input func
a
b
c
y
00 01 11 10
0
1
ab
c
4-input func
a
b
c
y
00 01 11 10
00
01
ab
cd
d
11
10

## Slide 39: Minimization with Karnaugh maps (1)
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields
  abc + abc + abc + abc

## Slide 40: Minimization with Karnaugh maps (2)
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields
  abc + abc + abc + abc
Karnaugh maps identify which inputs are (ir)relevant to the output
0 | 0 | 0 | 1
1 | 1 | 0 | 1
00 01 11 10
0
1
c
ab

## Slide 41: Minimization with Karnaugh maps (2)
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields
  abc + abc + abc + abc
Karnaugh map minimization
  Cover all 1’s
  Group adjacent blocks of 2n 1’s that yield a rectangular shape
  Encode the common features of the rectangle
    out = ab + ac
0 | 0 | 0 | 1
1 | 1 | 0 | 1
00 01 11 10
0
1
c
ab

## Slide 42: Karnaugh Minimization Tricks (1)
0 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab
1 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab

## Slide 43: Karnaugh Minimization Tricks (1)
Minterms can overlap
  out = bc + ac + ab
Minterms can span 2, 4, 8 or more cells
  out = c + ab
0 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab
1 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab

## Slide 44: Karnaugh Minimization Tricks (2)
1 | 0 | 0 | 1
0 | 0 | 0 | 0
0 | 0 | 0 | 0
1 | 0 | 0 | 1
00 01 11 10
00
01
ab
cd
11
10
0 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 0 | 1
0 | 0 | 0 | 0
00 01 11 10
00
01
ab
cd
11
10

## Slide 45: Karnaugh Minimization Tricks (2)
The map wraps around
  out = bd
  out = bd
1 | 0 | 0 | 1
0 | 0 | 0 | 0
0 | 0 | 0 | 0
1 | 0 | 0 | 1
00 01 11 10
00
01
ab
cd
11
10
0 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 0 | 1
0 | 0 | 0 | 0
00 01 11 10
00
01
ab
cd
11
10

## Slide 46: Karnaugh Minimization Tricks (3)
“Don’t care” values can be interpreted individually in whatever way is convenient
  assume all x’s = 1
  out = d
  assume middle x’s = 0
  assume 4th column x = 1
  out = bd
1 | 0 | 0 | x
0 | x | x | 0
0 | x | x | 0
1 | 0 | 0 | 1
00 01 11 10
00
01
ab
cd
11
10
0 | 0 | 0 | 0
1 | x | x | x
1 | x | x | 1
0 | 0 | 0 | 0
00 01 11 10
00
01
ab
cd
11
10

## Slide 47: Multiplexer
A multiplexer selects between multiple inputs
  out = a, if d = 0
  out = b, if d = 1
Build truth table
Minimize diagram
Derive logic diagram
a
b
d

## Slide 48: Multiplexer Implementation
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Build a truth table
  = abd + abd + a bd + a b d
a
b
d

## Slide 49: Multiplexer Implementation
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Build the Karnaugh map
a
b
d
0 | 0 | 1 | 1
0 | 1 | 1 | 0
00 01 11 10
0
1
d
ab

## Slide 50: Multiplexer Implementation
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Derive Minimal Logic Equation
  out = ad + bd
a
b
d
0 | 0 | 1 | 1
0 | 1 | 1 | 0
00 01 11 10
0
1
d
ab

## Slide 51: Multiplexer Implementation
d
out
b
a
00 01 11 10
0
1
d
ab
Derive Minimal Logic Equation
  out = ad + bd
0 | 0 | 1 | 1
0 | 1 | 1 | 0
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
a
b
d

## Slide 52: Summary
We can now implement any logic circuit
  Can do it efficiently, using Karnaugh maps to find the minimal terms required
  Can use either NAND or NOR gates to implement the logic circuit
  Can use P- and N-transistors to implement NAND or NOR gates