## Slide 1: Arithmetic
Hakim Weatherspoon
CS 3410, Spring 2012
Computer Science
Cornell University
See P&H 2.4 (signed), 2.5, 2.6, C.6, and Appendix C.6

## Slide 2: Goals for today
Binary (Arithmetic) Operations
  One-bit and four-bit adders
  Negative numbers and two’s compliment
  Addition (two’s compliment)
  Subtraction (two’s compliment)
  Performance

## Slide 3: Binary Addition
Addition works the same way regardless of base
  Add the digits in each position
  Propagate the carry
  Unsigned binary addition is pretty easy
  Combine two bits at a time
  Along with a carry
183 + 254
001110
+ 011100

## Slide 4: 1-bit Adder
Half Adder
Adds two 1-bit numbers
Computes 1-bit result and 1-bit carry
A
B
R
C
Notes: Adds two 1-bit numbers, computes 1-bit result and carry out
Useful for the rightmost binary digit, not much else

## Slide 5: 1-bit Adder with Carry
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded
A
B
R
Cout
Cin

## Slide 6: 4-bit Adder
4-Bit Full Adder
Adds two 4-bit numbers and carry in
Computes 4-bit result and carry out
Can be cascaded
A[4]
B[4]
R[4]
Cout
Cin
Notes: Adds two 1-bit numbers, along with carry-in, computes 1-bit result and carry out
Can be cascaded to add N-bit numbers

## Slide 7: 4-bit Adder
Adds two 4-bit numbers, along with carry-in
Computes 4-bit result and carry out
Carry-out = overflow indicates result does not fit in 4 bits
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
Cout
Cin

## Slide 8: Arithmetic with Negative Numbers
Negative Numbers Complicate Arithmetic
Recall addition with negatives:

## Slide 9: Arithmetic with Negative Numbers
Negative Numbers Complicate Arithmetic
Recall addition with negatives:
  pos + pos  add magnitudes, result positive
  neg + neg  add magnitudes, result negative
  pos + neg  subtract smaller magnitude, keep sign of bigger magnitude

## Slide 10: First Attempt: Sign/Magnitude Representation
First Attempt: Sign/Magnitude Representation
1 bit for sign (0=positive, 1=negative)
N-1 bits for magnitude
Notes: problems? two zeros, circuit still complicated

## Slide 11: Two’s Complement Representation
Better: Two’s Complement Representation
Leading 1’s for negative numbers
To negate any number:
    complement all the bits
    then add 1
Notes: add 1 and *discard carry*

## Slide 12: Two’s Complement
Non-negatives
(as usual):
+0 = 0000
+1 = 0001
+2 = 0010
+3 = 0011
+4 = 0100
+5 = 0101
+6 = 0110
+7 = 0111
+8 = 1000
Negatives
(two’s complement: flip then add 1):
Notes: choose -8 so we have a sign bit
+0 = -0
wraps from +7 to -8
asymmetric: no +8

## Slide 13: Two’s Complement
Non-negatives
(as usual):
+0 = 0000
+1 = 0001
+2 = 0010
+3 = 0011
+4 = 0100
+5 = 0101
+6 = 0110
+7 = 0111
+8 = 1000
Negatives
(two’s complement: flip then add 1):
~0 = 1111 -0 = 0000
~1 = 1110 -1 = 1111
~2 = 1101 -2 = 1110
~3 = 1100 -3 = 1101
~4 = 1011 -4 = 1100
~5 = 1010 -5 = 1011
~3 = 1001 -6 = 1010
~7 = 1000 -7 = 1001
~8 = 0111 -8 = 1000
Notes: choose -8 so we have a sign bit
+0 = -0
wraps from +7 to -8
asymmetric: no +8

## Slide 14: Two’s Complement Facts
Signed two’s complement
  Negative numbers have leading 1’s
  zero is unique: +0 = - 0
  wraps from largest positive to largest negative
N bits can be used to represent
  unsigned:
    eg: 8 bits 
  signed (two’s complement):
    ex: 8 bits 

## Slide 15: Sign Extension & Truncation
Extending to larger size
Truncate to smaller size
  Copy the leftmost bit into new leading bits
    For positive number, put 0’s in new leading bits
    For negative number, put 1’s in new leading bits
  Drop leading bits so long as sign doesn’t change

## Slide 16: Two’s Complement Addition
Addition with two’s complement signed numbers
Perform addition as usual, regardless of sign (it just works)
Notes: 1 + (-1)
(-3) + (-1)
(-7) + 3
7 + (-3)
7 + 1 : overflow
(-7) + (-3) : overflow
(-7) + (-1)

## Slide 17: Two’s Complement Addition
Addition with two’s complement signed numbers
Perform addition as usual, regardless of sign (it just works)
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
Cout
Notes: 1 + (-1)
(-3) + (-1)
(-7) + 3
7 + (-3)
7 + 1 : overflow
(-7) + (-3) : overflow
(-7) + (-1)

## Slide 18: Overflow
Overflow
  adding a negative and a positive?
  adding two positives?
  adding two negatives?

## Slide 19: Overflow
Overflow
  adding a negative and a positive?
  adding two positives?
  adding two negatives?
Rule of thumb:
Overflow happened iff carry into msb != carry out of msb

## Slide 20: Two’s Complement Adder
Two’s Complement Adder with overflow detection
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
over flow
0

## Slide 21: Binary Subtraction
Two’s Complement Subtraction
Notes: a – b, where b is so large that –B overflows
B must be -8, so that –B = -8
last bit will change
if a >= 0, will correctly signal overflow
if a < 0, will correctly subtract and not signal overflow

## Slide 22: Binary Subtraction
Two’s Complement Subtraction
A – B = A + (-B) = A + (B + 1)
R0
R1
R2
R3
over flow
1
A0
B0
A1
B1
A2
B2
A3
B3
Q: What if (-B) overflows?
Notes: a – b, where b is so large that –B overflows
B must be -8, so that –B = -8
last bit will change
if a >= 0, will correctly signal overflow
if a < 0, will correctly subtract and not signa l overflow

## Slide 23: A Calculator
decoder
8
8
S 0=add
1=sub
A
B
8
Notes: User enters the numbers to be added or subtracted using toggle switches
User selects ADD or SUBTRACT
Muxes feed A and B, or A and –B, to the 8-bit adder
The 8-bit decoder for the hex display is straightforward (but not shown in detail)

## Slide 24: A Calculator
adder
mux
decoder
8
8
8
8
8
S
A
B
8
0=add
1=sub
Notes: red herring? constants into mux

## Slide 25: Efficiency and Generality
  Is this design fast enough?
  Can we generalize to 32 bits? 64? more?
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
C0

## Slide 26: Performance
Speed of a circuit is affected by the number of gates in series (on the critical path or the deepest level of logic)
Combinational
Logic
tcombinational
inputs arrive
outputs expected

## Slide 27: 4-bit Ripple Carry Adder
A3
B3
R3
C4
A1
B1
R1
A2
B2
R2
A0
B0
C0
R0
C1
C2
C3
First full adder, 2 gate delay
Second full adder, 2 gate delay
…
Carry ripples from lsb to msb

## Slide 28: Critical Path
Which operation is the critical path?
A) ADD/SUB
B) AND
C) OR
D) LT

## Slide 29: Critical Path
What is the length of the critical path (in gates)?
(counting inverters)
A) 3
B) 5
C) 9
D) 11

## Slide 30: Critical Path
What is the length of the critical path for a 32-bit ALU (in gates)? (counting inverters)
A) 11
B) 32
C) 64
D) 71

## Slide 31: Recap
We can now implement any combinational (combinatorial) logic circuit
  Decompose large circuit into manageable blocks
    Encoders, Decoders, Multiplexors, Adders, ...
  Design each block
    Binary encoded numbers for compactness
  Can implement circuits using NAND or NOR gates
  Can implement gates using use P- and N-transistors
  And can add and subtract numbers (in two’s compliment)!
  Next, state and finite state machines…

## Slide 32: Administrivia
Make sure you are
Registered for class, can access CMS
Have a Section you can go to
Have project partner in same Lab Section
Lab1 and HW1 are out
Both due in one week, next Monday, start early
Work alone
But, use your resources
  Lab Section, Piazza.com, Office Hours, Homework Help Session,
  Class notes, book, Sections, CSUGLab
Homework Help Session
Wednesday and Friday from 3:30-5:30pm
Location: 203 Thurston

## Slide 33: Administrivia
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2012sp/schedule.html
Slides and Reading for lectures
Office Hours
Homework and Programming Assignments
Prelims (in evenings):
  Tuesday, February 28th
  Thursday, March 29th
  Thursday, April 26th
Schedule is subject to change

## Slide 34: Stateful Components
Until now is combinatorial logic
  Output is computed when inputs are present
  System has no internal state
  Nothing computed in the present can depend on what happened in the past!
Need a way to record data
Need a way to build stateful circuits
Need a state-holding device
Finite State Machines
Inputs
Combinational circuit
Outputs
N
M
Notes: How are we going to stably store state

## Slide 35: How can we store and change values?
(a)
(b)
(c)
B
A
C
Ballots
How do we create
vote counter
machine
detect
enc
8
3
7
7LED decode
A
B
S
R
Q
Q
(d) All the above
(e) None

## Slide 36: Unstable Devices
B
A
C

## Slide 37: Bistable Devices
In stable state, A = B
How do we change the state?
A
B
A
B
1
A
B
1
0
0
A Simple Device
Stable and unstable equilibria?
Notes: How to create state? Feedback.
Show how the signal works

## Slide 38: SR Latch
Set-Reset (SR) Latch
Stores a value Q and its complement Q
S | R | Q | Q
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S
R
Q
Q
S
R
Q
Q
Notes: Start with 0, 1 => 0, 1
then 0, 0 => 0, 1
then 1, 0 => 1, 0
then 0, 0 => 1, 0, better yet “stay”
1, 1 is forbidden, b/c going to 0, 0 after goes haywire

## Slide 39: SR Latch
Set-Reset (SR) Latch
Stores a value Q and its complement Q
S | R | Q | Q
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S
R
Q
Q
S
R
Q
Q
Notes: Start with 0, 1 => 0, 1
then 0, 0 => 0, 1
then 1, 0 => 1, 0
then 0, 0 => 1, 0, better yet “stay”
1, 1 is forbidden, b/c going to 0, 0 after goes haywire

## Slide 40: Unclocked D Latch
Data (D) Latch
D | Q | Q
0 |  | 
1 |  | 
S
R
D
Q
Q
Notes: Start in 0, 0, 1
Change to D = 1
After NOT gate, R = 0
After OR+NOT gates, /Q = 0 (R is already ready then), Q goes to 1
Problem: No way to hold state

## Slide 41: Unclocked D Latch
Data (D) Latch
D | Q | Q
0 | 0 | 1
1 | 1 | 0
S
R
D
Q
Q
Data Latch
  Easier to use than an SR latch
  No possibility of entering an undefined state
When D changes, Q changes
    … immediately (after a delay of 2 Ors and 2 NOTs)
Need to control when the output changes
Notes: Start in 0, 0, 1
Change to D = 1
After NOT gate, R = 0
After OR+NOT gates, /Q = 0 (R is already ready then), Q goes to 1
Problem: No way to hold state

## Slide 42: D Latch with Clock
S
R
D
clk
Q
Q
clk
D
Q
Level Sensitive D Latch
Clock high: set/reset (according to D)
Clock low: keep state (ignore D)
Notes: Any forbidden S=R=1 inputs? no

## Slide 43: D Latch with Clock
S
R
D
clk
Q
Q
S | R | Q | Q
0 | 0 | Q | Q
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | forbidden | 
D | Q | Q
0 | 0 | 1
1 | 1 | 0
clk | D | Q | Q
0 | 0 | Q | Q
0 | 1 | Q | Q
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 44: D Latch with Clock
S
R
D
clk
Q
Q
D | Q | Q
0 | 0 | 1
1 | 1 | 0
clk | D | Q | Q
0 | 0 | Q | Q
0 | 1 | Q | Q
1 | 0 | 0 | 1
1 | 1 | 1 | 0
clk
D
Q
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 45: Clocks
Clock helps coordinate state changes
  Usually generated by an oscillating crystal
  Fixed period; frequency = 1/period
period
high
low
1
0
falling edge
rising edge

## Slide 46: Edge-triggering
Can design circuits to change on the rising or falling edge
Trigger on rising edge = positive edge-triggered
Trigger on falling edge = negative edge-triggered
Inputs must be stable just before the triggering edge
input
clock

## Slide 47: Clock Methodology
Clock Methodology
Negative edge, synchronous
    Signals must be stable near falling clock edge
Positive edge synchronous
Asynchronous, multiple clocks, . . .
clk
compute
save
tsetup
thold
compute
save
compute
tcombinational

## Slide 48: Edge-Triggered D Flip-Flop
D Flip-Flop
Edge-Triggered
Data is captured when clock is high
Outputs change only on falling edges
D
Q
Q
D
Q
Q
c
F
L
L
clk
D
F
Q
c
Q
Q
D
clk

## Slide 49: Clock Disciplines
Level sensitive
  State changes when clock is high (or low)
Edge triggered
  State changes at clock edge
positive edge-triggered
negative edge-triggered

## Slide 50: Registers
Register
D flip-flops in parallel
shared clock
extra clocked inputs: write_enable, reset, …
clk
D0
D3
D1
D2
4
4
4-bit
reg

## Slide 51: An Example: What will this circuit do?
32-bit
reg
Clk
+1
Run
WE
R
Reset
Decoder