## Slide 1: Caches
Hakim Weatherspoon
CS 3410, Spring 2012
Computer Science
Cornell University
See P&H 5.1, 5.2 (except writes)

## Slide 2: Administrivia
HW4 due today , March 27th
Project2 due next Monday, April 2nd
Prelim2
  Thursday, March 29th at 7:30pm in Philips 101
  Review session today 5:30-7:30pm in Phillips 407

## Slide 3: Big Picture: Memory
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Memory: big & slow vs Caches: small & fast

## Slide 4: Goals for Today: caches
Caches vs memory vs tertiary storage
  Tradeoffs: big & slow vs small & fast
    Best of both worlds
  working set: 90/10 rule
  How to predict future: temporal & spacial locality
Examples of caches:
  Direct Mapped
  Fully Associative
  N-way set associative

## Slide 5: Performance
CPU clock rates ~0.2ns – 2ns (5GHz-500MHz)
Technology Capacity $/GB Latency
Tape 1 TB $.17 100s of seconds
Disk 2 TB $.03 Millions of cycles (ms)
SSD (Flash) 128 GB $2 Thousands of cycles (us)
DRAM 8 GB $10 (10s of ns)
SRAM off-chip 8 MB $4000 5-15 cycles (few ns)
SRAM on-chip 256 KB ??? 1-3 cycles (ns)
Others: eDRAM aka 1T SRAM , FeRAM, CD, DVD, …
Q: Can we create illusion of cheap + large + fast?
50-300 cycles
Notes: Capacity and latency are closely coupled
Cost is inversely proportional
eDRAM is embedded DRAM that is part of the same ASIC and die instead of a separate module
1T-SRAM, stands for 1-transistor SRAM, is an instance eDRAM where the refresh controller is integrated so the memory can externally be treated as SRAM.

## Slide 6: Memory Pyramid
Memory Pyramid
Disk (Many GB – few TB)
Memory (128MB – few GB)
L2 Cache (½-32MB)
RegFile
100s bytes
< 1 cycle access
1-3 cycle access
5-15 cycle access
50-300 cycle access
L3 becoming more common (eDRAM ?)
These are rough numbers: mileage may vary for latest/greatest Caches usually made of SRAM (or eDRAM)
L1 Cache
(several KB)
1000000+ cycle access
Notes: L1 L2 and even L3 all on-chip these days using SRAM and eDRAM

## Slide 7: Memory Hierarchy
Memory closer to processor
  small & fast
  stores active data
Memory farther from processor
  big & slow
  stores inactive data

## Slide 8: Memory Hierarchy
Insight for Caches
If Mem[x] is was accessed recently...
… then Mem[x] is likely to be accessed soon
  Exploit temporal locality:
    Put recently accessed Mem[x] higher in memory hierarchy
    since it will likely be accessed again soon
… then Mem[x ± ε] is likely to be accessed soon
  Exploit spatial locality:
    Put entire block containing Mem[x] and surrounding addresses higher in memory hierarchy since nearby address will likely
    be accessed
put entire block containing Mem[x] higher in the pyramid
put recently accessed Mem[x] higher in the pyramid
A: Data that will be used soon
Notes: soon = frequency of loads

## Slide 9: Memory Hierarchy
Memory closer to processor is fast but small
  usually stores subset of memory farther away
    “strictly inclusive”
  Transfer whole blocks (cache lines):
  4kb: disk ↔ ram
  256b: ram ↔ L2
  64b: L2 ↔ L1

## Slide 10: Memory Hierarchy
Memory trace
0x7c9a2b18
0x7c9a2b19
0x7c9a2b1a
0x7c9a2b1b
0x7c9a2b1c
0x7c9a2b1d
0x7c9a2b1e
0x7c9a2b1f
0x7c9a2b20
0x7c9a2b21
0x7c9a2b22
0x7c9a2b23
0x7c9a2b28
0x7c9a2b2c
0x0040030c
0x00400310
0x7c9a2b04
0x00400314
0x7c9a2b00
0x00400318
0x0040031c
...
int n = 4;
int k[] = { 3, 14, 0, 10 };
int fib(int i) {
  if (i <= 2) return i;
  else return fib(i-1)+fib(i-2);
}
int main(int ac, char **av) {
for (int i = 0; i < n; i++) {
printi(fib(k[i]));
prints("\n");
}
}

## Slide 11: Cache Lookups (Read)
Processor tries to access Mem[x]
Check: is block containing Mem[x] in the cache?
  Yes: cache hit
    return requested data from cache line
  No: cache miss
    read block from memory (or lower level cache)
    (evict an existing cache line to make room)
    place new block in cache
    return requested data
     and stall the pipeline while all of this happens

## Slide 12: Three common designs
A given data block can be placed…
  … in exactly one cache line  Direct Mapped
  … in any cache line  Fully Associative
  … in a small set of cache lines  Set Associative

## Slide 13: Direct Mapped Cache
Direct Mapped Cache
  Each block number mapped to a single cache line index
  Simplest hardware
line 0 |  |  |  | 
line 1 |  |  |  | 
0x000000 | 
0x000004 | 
0x000008 | 
0x00000c | 
0x000010 | 
0x000014 | 
0x000018 | 
0x00001c | 
0x000020 | 
0x000024 | 
0x000028 | 
0x00002c | 
0x000030 | 
0x000034 | 
0x000038 | 
0x00003c | 
0x000040 | 
0x000044 | 
0x000048 | 
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 14: Direct Mapped Cache
Direct Mapped Cache
  Each block number mapped to a single cache line index
  Simplest hardware
line 0 |  | 
line 1 |  | 
line 2 |  | 
line 3 |  | 
0x000000 | 
0x000004 | 
0x000008 | 
0x00000c | 
0x000010 | 
0x000014 | 
0x000018 | 
0x00001c | 
0x000020 | 
0x000024 | 
0x000028 | 
0x00002c | 
0x000030 | 
0x000034 | 
0x000038 | 
0x00003c | 
0x000040 | 
0x000044 | 
0x000048 | 
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 15: Direct Mapped Cache

## Slide 16: Direct Mapped Cache (Reading)
V
Tag
Block
=
Tag Index Offset
word select
hit?
data
=
hit?
data
word select
32bits

## Slide 17: Example:A Simple Direct Mapped Cache
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
tag data
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
4 cache lines
2 word block
0
0
0
0
V
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 18: Example:A Simple Direct Mapped Cache
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
tag data
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
4 cache lines
2 word block
2 bit tag field
2 bit index field
1 bit block offset
0
0
0
0
V
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 19: 1st Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Cache
Processor
tag data
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
0
0
0
0
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
V
Misses:
Hits:

## Slide 20: 8th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 10 ]
LB $2  M[ 15 ]
LB $2  M[ 8 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
Cache
tag data
150
140
1
0
0
V
Misses:
Hits:

## Slide 21: Misses
Three types of misses
  Cold (aka Compulsory)
    The line is being referenced for the first time
  Capacity
    The line was evicted because the cache was not large enough
  Conflict
    The line was evicted because of another access whose index conflicted

## Slide 22: Misses
Q: How to avoid…
Cold Misses
  Unavoidable? The data was never in the cache…
  Prefetching!
Capacity Misses
  Buy more SRAM
Conflict Misses
  Use a more flexible cache design

## Slide 23: Direct Mapped Example: 6th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
2
150
140
1
0
0
V
Using byte addresses in this example! Addr Bus = 5 bits
Pathological example

## Slide 24: 10th and 11th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
LB $2  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Cache
tag data
2
150
140
1
0
0
V
Misses:
Hits:

## Slide 25: Cache Organization
How to avoid Conflict Misses
Three common designs
  Fully associative: Block can be anywhere in the cache
  Direct mapped: Block can only be in one line in the cache
  Set-associative: Block can be in a few (2 to 8) places in the cache

## Slide 26: Example:Simple Fully Associative Cache
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
tag data
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
4 cache lines
2 word block
4 bit tag field
1 bit block offset
V
V
V
V
V
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 27: 1st Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
tag data
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
0
0
0
0
V
Misses:
Hits:

## Slide 28: 10th and 11th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
LB $2  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
0
V

## Slide 29: Fully Associative Cache (Reading)
V
Tag
Block
word select
hit?
data
line select
=
=
=
=
32bits
64bytes
Tag Offset
Notes: “way” = line

## Slide 30: Eviction
Which cache line should be evicted from the cache to make room for a new line?
  Direct-mapped
    no choice, must evict line selected by index
  Associative caches
    random: select one of the lines at random
    round-robin: similar to random
    FIFO: replace oldest line
    LRU: replace line that has not been used in the longest time

## Slide 31: Cache Tradeoffs
Direct Mapped
+ Smaller
+ Less
+ Less
+ Faster
+ Less
+ Very
– Lots
– Low
– Common
Fully Associative
Larger –
More –
More –
Slower –
More –
Not Very –
Zero +
High +
?
Tag Size
SRAM Overhead
Controller Logic
Speed
Price
Scalability
# of conflict misses
Hit rate
Pathological Cases?

## Slide 32: Compromise
Set-associative cache
Like a direct-mapped cache
  Index into a location
  Fast
Like a fully-associative cache
  Can store multiple entries
    decreases thrashing in cache
  Search in each element

## Slide 33: Comparison: Direct Mapped
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
2
100
110
150
140
1
0
0
4 cache lines
2 word block
2 bit tag field
2 bit index field
1 bit block offset field
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 34: Comparison: Fully Associative
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
0
4 cache lines
2 word block
4 bit tag field
1 bit block offset field
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 35: Comparison: 2 Way Set Assoc
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
0
0
0
0
2 sets
2 word block
3 bit tag field
1 bit set index field
1 bit block offset field
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
Using byte addresses in this example! Addr Bus = 5 bits
Notes: 0001 M: 1, H: 0
0101 M: 2, H: 0
0001 M: 2, H: 3 01/45/00/00
1100 M: 3, H: 3 12,13/01/00/00
1000 M:4, H:3 12,13/4,5/00/00
0100 M:5, H:3 8,9/45/00/00
0000 M:5, H:4 01/45/00/00
1100 M: 3, H: 3 12,13/01/00/00
1000 M:4, H:3 8,9/12,13/00/00
M:7,H:4

## Slide 36: 3-Way Set Associative Cache (Reading)
word select
hit?
data
line select
=
=
=
32bits
64bytes
Tag Index Offset

## Slide 37: Remaining Issues
To Do:
  Evicting cache lines
  Picking cache parameters
  Writing using the cache

## Slide 38: Summary
Caching assumptions
  small working set: 90/10 rule
  can predict future: spatial & temporal locality
Benefits
  big & fast memory built from (big & slow) + (small & fast)
Tradeoffs: associativity, line size, hit cost, miss penalty, hit rate
  Fully Associative  higher hit cost, higher hit rate
  Larger block size  lower hit cost, higher miss penalty
Next up: other designs; writing to caches