## Slide 1: Virtual Memory 2
Hakim Weatherspoon
CS 3410, Spring 2012
Computer Science
Cornell University
P & H Chapter 5.4

## Slide 2: Goals for Today
Virtual Memory
  Address Translation
    Pages, page tables, and memory mgmt unit
  Paging
  Role of Operating System
    Context switches, working set, shared memory
  Performance
    How slow is it
    Making virtual memory fast
    Translation lookaside buffer (TLB)
  Virtual Memory Meets Caching

## Slide 3
Role of the Operating System
Context switches, working set,
shared memory

## Slide 4: Role of the Operating System
The operating systems (OS) manages and multiplexes memory between process. It…
  Enables processes to (explicitly) increase memory: sbrk and (implicitly) decrease memory
  Enables sharing of physical memory: multiplexing memory via context switching, sharing memory, and paging
  Enables and limits the number of processes that can run simultaneously

## Slide 5: sbrk
Suppose Firefox needs a new page of memory
(1) Invoke the Operating System
  void *sbrk(int nbytes);
(2) OS finds a free page of physical memory
  clear the page (fill with zeros)
  add a new entry to Firefox’s PageTable

## Slide 6: Context Switch
Suppose Firefox is idle, but Skype wants to run
(1) Firefox invokes the Operating System
  int sleep(int nseconds);
(2) OS saves Firefox’s registers, load skype’s
  (more on this later)
(3) OS changes the CPU’s Page Table Base Register
  Cop0:ContextRegister / CR3:PDBR
(4) OS returns to Skype

## Slide 7: Shared Memory
Suppose Firefox and Skype want to share data
(1) OS finds a free page of physical memory
  clear the page (fill with zeros)
  add a new entry to Firefox’s PageTable
  add a new entry to Skype’s PageTable
    can be same or different vaddr
    can be same or different page permissions

## Slide 8: Multiplexing
Suppose Skype needs a new page of memory, but Firefox is hogging it all
(1) Invoke the Operating System
  void *sbrk(int nbytes);
(2) OS can’t find a free page of physical memory
  Pick a page from Firefox instead (or other process)
(3) If page table entry has dirty bit set…
  Copy the page contents to disk
(4) Mark Firefox’s page table entry as “on disk”
  Firefox will fault if it tries to access the page
(5) Give the newly freed physical page to Skype
  clear the page (fill with zeros)
  add a new entry to Skyps’s PageTable

## Slide 9: Paging Assumption 1
OS multiplexes physical memory among processes
  assumption # 1: processes use only a few pages at a time
  working set = set of process’s recently actively pages
# recent accesses
0x00000000
0x90000000

## Slide 10: Thrashing (excessive paging)
Q: What if working set is too large?
Case 1: Single process using too many pages
Case 2: Too many processes
working set
mem
disk
swapped
P1
working set
mem
disk
swapped
ws
mem
disk
ws
ws
ws
ws
ws

## Slide 11: Thrashing
Thrashing b/c working set of process (or processes) greater than physical memory available
    Firefox steals page from Skype
    Skype steals page from Firefox
  I/O (disk activity) at 100% utilization
    But no useful work is getting done
Ideal: Size of disk, speed of memory (or cache)
Non-ideal: Speed of disk

## Slide 12: Paging Assumption 2
OS multiplexes physical memory among processes
  assumption # 2: recent accesses predict future accesses
  working set usually changes slowly over time
working set
time 

## Slide 13: More Thrashing
Q: What if working set changes rapidly or unpredictably?
A: Thrashing b/c recent accesses don’t predict future accesses
working set
time 

## Slide 14: Preventing Thrashing
How to prevent thrashing?
  User: Don’t run too many apps
  Process: efficient and predictable mem usage
  OS: Don’t over-commit memory, memory-aware scheduling policies, etc.

## Slide 15
Performance

## Slide 16: Performance
Virtual Memory Summary
PageTable for each process:
  4MB contiguous in physical memory, or multi-level, …
  every load/store translated to physical addresses
  page table miss = page fault load the swapped-out page and retry instruction, or kill program if the page really doesn’t exist, or tell the program it made a mistake

## Slide 17: Page Table Review
x86 Example: 2 level page tables, assume… 32 bit vaddr, 32 bit paddr 4k PDir, 4k PTables, 4k Pages
Q:How many bits for a physical page number?
A: 20
Q: What is stored in each PageTableEntry?
A: ppn, valid/dirty/r/w/x/…
Q: What is stored in each PageDirEntry?
A: ppn, valid/?/…
Q: How many entries in a PageDirectory?
A: 1024 four-byte PDEs
Q: How many entires in each PageTable?
A: 1024 four-byte PTEs
PDE
PTBR
PDE
PDE
PDE
PTE
PTE
PTE
PTE
Notes: byte offset = 0x44c
PTI = 0x12a
PDI = 0x205

## Slide 18: Page Table Example
x86 Example: 2 level page tables, assume… 32 bit vaddr, 32 bit paddr 4k PDir, 4k PTables, 4k Pages PTBR = 0x10005000 (physical)
Write to virtual address 0x7192a44c… Q: Byte offset in page? PT Index? PD Index?
(1) PageDir is at 0x10005000, so… Fetch PDE from physical address 0x1005000+(4*PDI)
  suppose we get {0x12345, v=1, …}
(2) PageTable is at 0x12345000, so… Fetch PTE from physical address 0x12345000+(4*PTI)
  suppose we get {0x14817, v=1, d=0, r=1, w=1, x=0, …}
(3) Page is at 0x14817000, so… Write data to physical address? Also: update PTE with d=1
PDE
PTBR
PDE
PDE
PDE
PTE
PTE
PTE
PTE
0x1481744c
Notes: byte offset = 0x44c
PTI = 0x12a
PDI = (0x719 >> 2) = 0x1c6

## Slide 19: Performance
Virtual Memory Summary
PageTable for each process:
  4MB contiguous in physical memory, or multi-level, …
  every load/store translated to physical addresses
  page table miss: load a swapped-out page and retry instruction, or kill program
Performance?
  terrible: memory is already slow translation makes it slower
Solution?
  A cache, of course
Notes: 4x slower!
Pipelining? No. Parallelization? No.

## Slide 20
Making Virtual Memory Fast
  The Translation Lookaside Buffer (TLB)

## Slide 21: Translation Lookaside Buffer (TLB)
Hardware Translation Lookaside Buffer (TLB)
A small, very fast cache of recent address mappings
  TLB hit: avoids PageTable lookup
  TLB miss: do PageTable lookup, cache result for later

## Slide 22: TLB Diagram
V | R | W | X | D | 
0 |  |  |  |  | invalid
1 |  |  |  | 0 | 
0 |  |  |  |  | invalid
0 |  |  |  |  | invalid
1 |  |  |  | 0 | 
0 |  |  |  | 0 | 
1 |  |  |  | 1 | 
0 |  |  |  |  | invalid
V | R | W | X | D | tag | ppn
V |  | 
0 |  | invalid
0 |  | invalid
0 |  | invalid
1 |  | 
0 |  | invalid
1 |  | 
1 |  | 
0 |  | invalid

## Slide 23: A TLB in the Memory Hierarchy
(1) Check TLB for vaddr (~ 1 cycle)
(2) TLB Miss: traverse PageTables for vaddr
(3a) PageTable has valid entry for in-memory page
  Load PageTable entry into TLB; try again (tens of cycles)
(3b) PageTable has entry for swapped-out (on-disk) page
  Page Fault: load from disk, fix PageTable, try again (millions of cycles)
(3c) PageTable has invalid entry
  Page Fault: kill process
CPU
TLB
Lookup
Cache
Mem
Disk
PageTable
Lookup
(2) TLB Hit
  compute paddr, send to cache
Notes: TLB miss in hardware usually, but not always
PageTable stuff in software

## Slide 24: TLB Coherency
TLB Coherency: What can go wrong?
A: PageTable or PageDir contents change
  swapping/paging activity, new shared pages, …
A: Page Table Base Register changes
  context switch between processes
Notes: Fully transparent

## Slide 25: Translation Lookaside Buffers (TLBs)
When PTE changes, PDE changes, PTBR changes….
Full Transparency: TLB coherency in hardware
  Flush TLB whenever PTBR register changes [easy – why?]
  Invalidate entries whenever PTE or PDE changes [hard – why?]
TLB coherency in software
If TLB has a no-write policy…
  OS invalidates entry after OS modifies page tables
  OS flushes TLB whenever OS does context switch
Notes: process ID could just be the PTBR for the process

## Slide 26: TLB Parameters
TLB parameters (typical)
  very small (64 – 256 entries), so very fast
  fully associative, or at least set associative
  tiny block size: why?
Intel Nehalem TLB (example)
  128-entry L1 Instruction TLB, 4-way LRU
  64-entry L1 Data TLB, 4-way LRU
  512-entry L2 Unified TLB, 4-way LRU

## Slide 27
Virtual Memory meets Caching
  Virtually vs. physically addressed caches
  Virtually vs. physically tagged caches

## Slide 28: Virtually Addressed Caching
Q: Can we remove the TLB from the critical path?
A: Virtually-Addressed Caches
CPU
TLB
Lookup
Virtually
Addressed
Cache
Mem
Disk
PageTable
Lookup
Notes: A: have to flush entire cache on context switch
A:
Doing synonym updates requires significant hardware – essentially an associative lookup on the physical address tags to see if you have multiple hits

## Slide 29: Virtual vs. Physical Caches
CPU
Cache
SRAM
Memory
DRAM
addr
data
MMU
Cache
SRAM
MMU
CPU
Memory
DRAM
addr
data
Cache works on physical addresses
Cache works on virtual addresses
Q: What happens on context switch?
Q: What about virtual memory aliasing?
Q: So what’s wrong with physically addressed caches?
Notes: A1: Physically-addressed: nothing; Virtually-addressed: need to flush cache
A2: Physically-addressed: nothing; Virtually-addressed: problems

## Slide 30: Indexing vs. Tagging
Physically-Addressed Cache
  slow: requires TLB (and maybe PageTable) lookup first
Virtually-Indexed, Virtually Tagged Cache
  fast: start TLB lookup before cache lookup finishes
  PageTable changes (paging, context switch, etc.)
     need to purge stale cache lines (how?)
  Synonyms (two virtual mappings for one physical page)
     could end up in cache twice (very bad!)
Virtually-Indexed, Physically Tagged Cache
  ~fast: TLB lookup in parallel with cache lookup
  PageTable changes  no problem: phys. tag mismatch
  Synonyms  search and evict lines with same phys. tag
Virtually-Addressed Cache

## Slide 31: Typical Cache Setup
CPU
L2 Cache
SRAM
Memory
DRAM
addr
data
MMU
Typical L1: On-chip virtually addressed, physically tagged
Typical L2: On-chip physically addressed
Typical L3: On-chip …
L1 Cache
SRAM
TLB SRAM

## Slide 32: Summary of Caches/TLBs/VM
Caches, Virtual Memory, & TLBs
Where can block be placed?
  Direct, n-way, fully associative
What block is replaced on miss?
  LRU, Random, LFU, …
How are writes handled?
  No-write (w/ or w/o automatic invalidation)
  Write-back (fast, block at time)
  Write-through (simple, reason about consistency)
Notes: Where?
Caches: direct/n-way/fa
VM: fa, but with a table of contents to eliminate searches
TLB: fa
Replacement?
varied
Writes?
Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
VM: write-back
TLB: usually no-write

## Slide 33: Summary of Caches/TLBs/VM
Caches, Virtual Memory, & TLBs
Where can block be placed?
  Caches: direct/n-way/fully associative (fa)
  VM: fa, but with a table of contents to eliminate searches
  TLB: fa
What block is replaced on miss?
  varied
How are writes handled?
  Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
  VM: write-back
  TLB: usually no-write
Notes: Where?
Caches: direct/n-way/fa
VM: fa, but with a table of contents to eliminate searches
TLB: fa
Replacement?
varied
Writes?
Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
VM: write-back
TLB: usually no-write

## Slide 34: Summary of Cache Design Parameters
 | L1 | Paged Memory | TLB
Size (blocks) | 1/4k to 4k | 16k to 1M | 64 to 4k
Size (kB) | 16 to 64 | 1M to 4G | 2 to 16
Block size (B) | 16-64 | 4k to 64k | 4-32
Miss rates | 2%-5% | 10-4 to 10-5% | 0.01% to 2%
Miss penalty | 10-25 | 10M-100M | 100-1000

## Slide 35: Administrivia
Project3 available now
  Design Doc due next week, Monday, April 16th
  Schedule a Design Doc review Mtg now for next week
  Whole project due Monday, April 23rd
  Competition/Games night Friday, April 27th, 5-7pm
HW5 is due today Tuesday, April 10th
  Download updated version. Use updated version.
  Online Survey due today.
Lab3 was due yesterday Monday, April 9th
Prelim3 is in two and a half weeks, Thursday, April 26th
  Time and Location: 7:30pm in Olin Hall room 155
  Old prelims are online in CMS