## Slide 1: Caches 2
Hakim Weatherspoon
CS 3410, Spring 2013
Computer Science
Cornell University
P & H Chapter 5.1-5.3, 5.3-5.4, 5.8, Also, 5.13 & 5.17

## Slide 2: Big Picture: Memory
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory
$0 (zero)
$1 ($at)
$29 ($sp)
$31 ($ra)
Code Stored in Memory
(also, data and stack)

## Slide 3: Big Picture: Memory
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Memory: big & slow vs Caches: small & fast
$0 (zero)
$1 ($at)
$29 ($sp)
$31 ($ra)
Code Stored in Memory
(also, data and stack)
Stack, Data, Code
Stored in Memory

## Slide 4: Big Picture: Memory
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Memory: big & slow vs Caches: small & fast
$0 (zero)
$1 ($at)
$29 ($sp)
$31 ($ra)
Code Stored in Memory
(also, data and stack)
Stack, Data, Code
Stored in Memory
$$
$$

## Slide 5: Big Picture
How do we make the processor fast,
Given that memory is VEEERRRYYYY SLLOOOWWW!!

## Slide 6: Big Picture
How do we make the processor fast,
Given that memory is VEEERRRYYYY SLLOOOWWW!!
But, insight for Caches
If Mem[x] was accessed recently...
… then Mem[x] is likely to be accessed soon
  Exploit temporal locality:
    Put recently accessed Mem[x] higher in memory hierarchy
    since it will likely be accessed again soon
… then Mem[x ± ε] is likely to be accessed soon
  Exploit spatial locality:
    Put entire block containing Mem[x] and surrounding addresses higher in memory hierarchy since nearby address will likely be accessed

## Slide 7: Big Picture
How do we make the processor fast,
Given that memory is VEEERRRYYYY SLLOOOWWW!!
But, insight for Caches
  small working set: 90/10 rule
  can predict future: spatial & temporal locality
Benefits
  Abstraction: big & fast memory
    built from (big & slow memory; DRAM) + (small & fast cache; SRAM)

## Slide 8: Memory Hierarchy
< 1 cycle access
L2 Cache (½-32MB)
5-15 cycle access
150-200 cycle access
L3 becoming more common
*These are rough numbers, mileage may vary.
1-3 cycle access
L1 Cache
(several KB)
1000000+ cycle access
Disk (Many GB – few TB)
Memory (128MB – few GB)
RegFile
100s bytes

## Slide 9: Just like your Contacts!
* Will refer to this analogy using GREEN in the slides.
5-15 clicks
Favorites
1-3 clicks
Speed
Dial
Bunch of clicks
Google / Facebook / White Pages
~ 1 click
Last
Called
More clicks
Contacts

## Slide 10: Memory Hierarchy
L2/L3 Cache
SRAM
9% of data is
“active”
Memory DRAM
90% of data
inactive
(not accessed)
L1 Cache
SRAM-on-chip
1% of data most accessed
Favorites
9% of people called
Contacts
90% people rarely called
Speed Dial
1% most called people

## Slide 11: Memory Hierarchy
Memory closer to processor
  small & fast
  stores active data
Memory farther
from processor
  big & slow
  stores inactive data
L1 Cache
SRAM-on-chip
L2/L3 Cache
SRAM
Memory
DRAM
Speed Dial
small & fast
Contact List
big & slow

## Slide 12: Memory Hierarchy
L1 Cache
SRAM-on-chip
L2/L3 Cache
SRAM
Memory
DRAM
Memory closer to processor is fast but small
usually stores subset
of memory farther
  “strictly inclusive”
Transfer whole blocks (cache lines):
4kB: disk ↔ RAM
256B: RAM↔L2
64B: L2 ↔ L1

## Slide 13: Goals for Today: caches
Comparison of cache architectures:
  Direct Mapped
  Fully Associative
  N-way set associative
Caching Questions
  How does a cache work?
  How effective is the cache (hit rate/miss rate)?
  How large is the cache?
  How fast is the cache (AMAT=average memory access time)
Next time: Writing to the Cache
  Write-through vs Write-back
Notes: Caches vs memory vs tertiary storage
- Tradeoffs: big & slow vs small & fast
- working set: 90/10 rule
- How to predict future: temporal & spacial locality

## Slide 14: Next Goal
How do the different cache architectures compare?
  Cache Architecture Tradeoffs?
  Cache Size?
  Cache Hit rate/Performance?

## Slide 15: Cache Tradeoffs
A given data block can be placed…
  … in any cache line  Fully Associative
  (a contact maps to any speed dial number)
  … in exactly one cache line  Direct Mapped
  (a contact maps to exactly one speed dial number)
  … in a small set of cache lines  Set Associative
  (like direct mapped, a contact maps to exactly one speed dial number, but many different contacts can associate with the same speed dial number at the same time)

## Slide 16: Cache Tradeoffs
Direct Mapped
+ Smaller
+ Less
+ Less
+ Faster
+ Less
+ Very
– Lots
– Low
– Common
Fully Associative
Larger –
More –
More –
Slower –
More –
Not Very –
Zero +
High +
?
Tag Size
SRAM Overhead
Controller Logic
Speed
Price
Scalability
# of conflict misses
Hit rate
Pathological Cases?

## Slide 17: Cache Tradeoffs
Compromise: Set-associative cache
Like a direct-mapped cache
  Index into a location
  Fast
Like a fully-associative cache
  Can store multiple entries
    decreases thrashing in cache
  Search in each element

## Slide 18: Direct Mapped Cache
Speed Dial
Use the first letter to index!
Block Size: 1 Contact Number
Contacts
2 | ABC | Baker, J.
3 | DEF | Dunn, A.
4 | GHI | Gill, S.
5 | JKL | Jones, N.
6 | MNO | Mann, B.
7 | PQRS | Powell, J.
8 | TUV | Taylor, B.
9 | WXYZ | Wright, T.
Baker, J. | 111-111-1111
Baker, S. | 222-222-2222
Dunn, A. | 333-333-3333
Foster, D. | 444-444-4444
Gill, D. | 555-555-5555
Harris, F. | 666-666-6666
Jones, N. | 777-777-7777
Lee, V. | 888-888-8888
Mann, B. | 111-111-1119
Moore, F. | 222-222-2229
Powell, C. | 333-333-3339
Sam, J. | 444-444-4449
Taylor, B. | 555-555-5559
Taylor, O. | 666-666-6669
Wright, T. | 777-777-7779
Zhang, W. | 888-888-8889
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 19: Fully Associative Cache
Speed Dial
No index!
Block Size: 1 Contact Number
Contacts
Baker, J.
Dunn, A.
Gill, S.
Jones, N.
Mann, B.
Powell, J.
Taylor, B.
Wright, T.
Baker, J. | 111-111-1111
Baker, S. | 222-222-2222
Dunn, A. | 333-333-3333
Foster, D. | 444-444-4444
Gill, D. | 555-555-5555
Harris, F. | 666-666-6666
Jones, N. | 777-777-7777
Lee, V. | 888-888-8888
Mann, B. | 111-111-1119
Moore, F. | 222-222-2229
Powell, C. | 333-333-3339
Sam, J. | 444-444-4449
Taylor, B. | 555-555-5559
Taylor, O. | 666-666-6669
Wright, T. | 777-777-7779
Zhang, W. | 888-888-8889
2
3
4
5
6
7
8
9
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 20: Fully Associative Cache
Speed Dial
No index!
Block Size: 1 Contact Number
Contacts
Mann, B.
Dunn, A.
Taylor, B.
Wright, T.
Baker, J.
Powell, J.
Gill, S.
Jones, N.
Baker, J. | 111-111-1111
Baker, S. | 222-222-2222
Dunn, A. | 333-333-3333
Foster, D. | 444-444-4444
Gill, D. | 555-555-5555
Harris, F. | 666-666-6666
Jones, N. | 777-777-7777
Lee, V. | 888-888-8888
Mann, B. | 111-111-1119
Moore, F. | 222-222-2229
Powell, C. | 333-333-3339
Sam, J. | 444-444-4449
Taylor, B. | 555-555-5559
Taylor, O. | 666-666-6669
Wright, T. | 777-777-7779
Zhang, W. | 888-888-8889
2
3
4
5
6
7
8
9
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 21: Fully Associative Cache
Speed Dial
Baker, J. | Baker, S.
Dunn, A. | Foster, D.
Gill, D. | Harris, F.
Jones, N. | Lee, V.
Mann, B. | Moore, F.
Powell, C. | Sam, J.
Taylor, B. | Taylor, O.
Wright, T. | Zhang, W.
No index!
Use the initial to offset!
Contacts
Block Size: 2 Contact Numbers
Baker, J. | 111-111-1111
Baker, S. | 222-222-2222
Dunn, A. | 333-333-3333
Foster, D. | 444-444-4444
Gill, D. | 555-555-5555
Harris, F. | 666-666-6666
Jones, N. | 777-777-7777
Lee, V. | 888-888-8888
Mann, B. | 111-111-1119
Moore, F. | 222-222-2229
Powell, C. | 333-333-3339
Sam, J. | 444-444-4449
Taylor, B. | 555-555-5559
Taylor, O. | 666-666-6669
Wright, T. | 777-777-7779
Zhang, W. | 888-888-8889
2
3
4
5
6
7
8
9
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 22: Fully Associative Cache
Speed Dial
Mann, B. | Moore, F.
Powell, C. | Sam, J.
Gill, D. | Harris, F.
Wright, T. | Zhang, W.
Baker, J. | Baker, S.
Dunn, A. | Foster, D.
Taylor, B. | Taylor, O.
Jones, N. | Lee, V.
No index!
Use the initial to offset!
Contacts
Block Size: 2 Contact Numbers
Baker, J. | 111-111-1111
Baker, S. | 222-222-2222
Dunn, A. | 333-333-3333
Foster, D. | 444-444-4444
Gill, D. | 555-555-5555
Harris, F. | 666-666-6666
Jones, N. | 777-777-7777
Lee, V. | 888-888-8888
Mann, B. | 111-111-1119
Moore, F. | 222-222-2229
Powell, C. | 333-333-3339
Sam, J. | 444-444-4449
Taylor, B. | 555-555-5559
Taylor, O. | 666-666-6669
Wright, T. | 777-777-7779
Zhang, W. | 888-888-8889
2
3
4
5
6
7
8
9
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 23: N-way Set Associative Cache
Speed Dial
2-way set associative cache
8 sets
Use the initial to offset!
Contacts
Block Size: 2 Contact Numbers
Baker, J. | 111-111-1111
Baker, S. | 222-222-2222
Dunn, A. | 333-333-3333
Foster, D. | 444-444-4444
Gill, D. | 555-555-5555
Harris, F. | 666-666-6666
Jones, N. | 777-777-7777
Lee, V. | 888-888-8888
Mann, B. | 111-111-1119
Moore, F. | 222-222-2229
Powell, C. | 333-333-3339
Sam, J. | 444-444-4449
Taylor, B. | 555-555-5559
Taylor, O. | 666-666-6669
Wright, T. | 777-777-7779
Zhang, W. | 888-888-8889
2
3
4
5
6
7
8
9
ABC
DEF
GHI
JKL
MNO
PQRS
TUV
WXYZ
Baker, J. | Baker, S.
Dunn, A. | Foster, D.
Gill, D. | Harris, F.
Jones, N. | Lee, V.
Mann, B. | Moore, F.
Powell, C. | Sam, J.
Taylor, B. | Taylor, O.
Wright, T. | Zhang, W.
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 24: N-way Set Associative Cache
Speed Dial
2-way set associative cache
8 sets
Use the initial to offset!
Contacts
Block Size: 2 Contact Numbers
Baker, J. | 111-111-1111
Baker, S. | 222-222-2222
Dunn, A. | 333-333-3333
Foster, D. | 444-444-4444
Gill, D. | 555-555-5555
Harris, F. | 666-666-6666
Henry, J. | 777-777-7777
Isaacs, M. | 888-888-8888
Mann, B. | 111-111-1119
Moore, F. | 222-222-2229
Powell, C. | 333-333-3339
Sam, J. | 444-444-4449
Taylor, B. | 555-555-5559
Taylor, O. | 666-666-6669
Wright, T. | 777-777-7779
Zhang, W. | 888-888-8889
2
3
4
5
6
7
8
9
ABC
DEF
GHI
JKL
MNO
PQRS
TUV
WXYZ
Baker, J. | Baker, S.
Dunn, A. | Foster, D.
Gill, D. | Harris, F.
Mann, B. | Moore, F.
Powell, C. | Sam, J.
Taylor, B. | Taylor, O.
Wright, T. | Zhang, W.
Henry, J. | Isaacs, M.
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 25: 2-Way Set Associative Cache (Reading)
word select
hit?
data
line select
=
=
32bits
64bytes
Tag Index Offset

## Slide 26: 3-Way Set Associative Cache (Reading)
word select
hit?
data
line select
=
=
=
32bits
64bytes
Tag Index Offset

## Slide 27: 3-Way Set Associative Cache (Reading)
Tag Index Offset
n bit index, m bit offset, N-way Set Associative
Q: How big is cache (data only)?

## Slide 28: 3-Way Set Associative Cache (Reading)
Tag Index Offset
n bit index, m bit offset, N-way Set Associative
Q: How much SRAM is needed (data + overhead)?

## Slide 29: Comparison: Direct Mapped
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
2
100
110
150
140
1
0
0
4 cache lines
2 word block
2 bit tag field
2 bit index field
1 bit block offset field
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 30: Comparison: Fully Associative
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
0
4 cache lines
2 word block
4 bit tag field
1 bit block offset field
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 31: Comparison: 2 Way Set Assoc
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
0
0
0
0
2 sets
2 word block
3 bit tag field
1 bit set index field
1 bit block offset field
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
Using byte addresses in this example! Addr Bus = 5 bits
Notes: 0001 M: 1, H: 0
0101 M: 2, H: 0
0001 M: 2, H: 3 01/45/00/00
1100 M: 3, H: 3 12,13/01/00/00
1000 M:4, H:3 12,13/4,5/00/00
0100 M:5, H:3 8,9/45/00/00
0000 M:5, H:4 01/45/00/00
1100 M: 3, H: 3 12,13/01/00/00
1000 M:4, H:3 8,9/12,13/00/00
M:7,H:4

## Slide 32: Misses
Cache misses: classification
The line is being referenced for the first time
  Cold (aka Compulsory) Miss
  The line was in the cache, but has been evicted…
  … because some other access with the same index
  Conflict Miss
… because the cache is too small
  i.e. the working set of program is larger than the cache
  Capacity Miss
Notes: Q: What causes a cache miss?
conflict: collisions, competition

## Slide 33: Takeaway
Direct Mapped  fast but low hit rate
Fully Associative  higher hit cost, but higher hit rate
N-way Set Associative  middleground

## Slide 34: Next Goal
Do larger caches and larger cachelines (aka cache blocks) increase hit rate?
Notes: Due to spatial locality?

## Slide 35: Larger Cachelines
Bigger does not always help
Mem access trace: 0, 16, 1, 17, 2, 18, 3, 19, 4, 20, …
Hit rate with four direct mapped 2-byte cache lines?
With eight 2-byte cache lines?
With two 4-byte cache lines?
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
10 | 
11 | 
12 | 
13 | 
14 | 
15 | 
16 | 
17 | 
18 | 
19 | 
20 | 
21 | 
line 0 |  | 
line 1 |  | 
line 2 |  | 
line 3 |  | 
line 0 |  |  |  | 
line 1 |  |  |  | 

## Slide 36: Larger Cachelines
Fully-associative reduces conflict misses...
… assuming good eviction strategy
Mem access trace: 0, 16, 1, 17, 2, 18, 3, 19, 4, 20, …
Hit rate with four fully-associative 2-byte cache lines?
… A larger block size can often increase hit rate
With two fully-associative 4-byte cache lines?
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
10 | 
11 | 
12 | 
13 | 
14 | 
15 | 
16 | 
17 | 
18 | 
19 | 
20 | 
21 | 
line 0 |  | 
line 1 |  | 
line 2 |  | 
line 3 |  | 
line 0 |  |  |  | 
line 1 |  |  |  | 
Notes: No temporal locality, but lots of spacial locality  larger blocks would help

## Slide 37: Larger Cachelines
… but large block size can still reduce hit rate
Mem access trace: 0, 100, 200, 1, 101, 201, 2, 102, 202,…
Hit rate with four fully-associative 2-byte cache lines?
With two fully-associative 4-byte cache lines?
line 0 |  | 
line 1 |  | 
line 2 |  | 
line 3 |  | 
line 0 |  |  |  | 
line 1 |  |  |  | 
Notes: e.g. a vector add

## Slide 38: Misses
Cache misses: classification
Cold (aka Compulsory)
  The line is being referenced for the first time
Capacity
  The line was evicted because the cache was too small
  i.e. the working set of program is larger than the cache
Conflict
  The line was evicted because of another access whose index conflicted
Notes: conflict can’t happen with fully associative
block size influences cold misses

## Slide 39: Next Goal
How to decide on Cache Organization
Q: How to decide block size?
A: Try it and see
But: depends on cache size, workload, associativity, …
Experimental approach!

## Slide 40: Experimental Results
Notes: Top to bottom: bigger cache means fewer misses.
For a given total cache size,
larger block sizes mean….
  fewer lines
  so fewer tags (and smaller tags for associative caches)
  so less overhead
  and fewer cold misses (within-block “prefetching”)
But
  fewer blocks available (for scattered accesses!)
  so more conflicts
  and miss penalty (time to fetch block) is larger

## Slide 41: Tradeoffs
For a given total cache size,
larger block sizes mean….
  fewer lines
  so fewer tags, less overhead
  and fewer cold misses (within-block “prefetching”)
But also…
  fewer blocks available (for scattered accesses!)
  so more conflicts
  and larger miss penalty (time to fetch block)
Notes: Same for other parameters: experimental mostly

## Slide 42: Associativity

## Slide 43: Other Designs
Multilevel caches

## Slide 44: Takeaway
Direct Mapped  fast but low hit rate
Fully Associative  higher hit cost, but higher hit rate
N-way Set Associative  middleground
Cacheline size matters. Larger cache lines can increase performance due to prefetching. BUT, can also decrease performance if working set size cannot fit in cache.

## Slide 45: Next Goal
Performance: What is the average memory access time (AMAT) for a cache?
AMAT = %hit x hit time + % miss x miss time

## Slide 46: Cache Performance Example
Average Memory Access Time (AMAT)
Cache Performance (very simplified):
L1 (SRAM): 512 x 64 byte cache lines, direct mapped
Data cost: 3 cycle per word access
Lookup cost: 2 cycle
Mem (DRAM): 4GB
Data cost: 50 cycle for first word, plus 3 cycles per subsequent word
16 words (i.e. 64 / 4 = 16)
Notes: Hit rate 90%
.90 *5 + .10*(2+50+16*3) = 4.5 + 10.0 = 14.5 cycles on average
Hit rate 95 %  9.5 cycles on average

## Slide 47: Cache Performance Example
Average Memory Access Time (AMAT)
Cache Performance (very simplified):
L1 (SRAM): 512 x 64 byte cache lines, direct mapped
Data cost: 3 cycle per word access
Lookup cost: 2 cycle
Mem (DRAM): 4GB
Data cost: 50 cycle for first word, plus 3 cycles per subsequent word
16 words (i.e. 64 / 4 = 16)
Notes: Hit rate 90%
.90 *5 + .10*(2+50+16*3) = 4.5 + 10.0 = 14.5 cycles on average
Hit rate 95 %  9.5 cycles on average

## Slide 48: Multi Level Caching
Cache Performance (very simplified):
L1 (SRAM): 512 x 64 byte cache lines, direct mapped
Hit time: 5 cycles
L2 cache: bigger
Hit time = 20 cycles
Mem (DRAM): 4GB
Hit rate: 90% in L1, 90% in L2
Often: L1 fast and direct mapped, L2 bigger and higher associativity

## Slide 49: Performance Summary
Average memory access time (AMAT)
depends on cache architecture and size
access time for hit,
miss penalty, miss rate
Cache design a very complex problem:
  Cache size, block size (aka line size)
  Number of ways of set-associativity (1, N, )
  Eviction policy
  Number of levels of caching, parameters for each
  Separate I-cache from D-cache, or Unified cache
  Prefetching policies / instructions
  Write policy

## Slide 50: Takeaway
Direct Mapped  fast but low hit rate
Fully Associative  higher hit cost, but higher hit rate
N-way Set Associative  middleground
Cacheline size matters. Larger cache lines can increase performance due to prefetching. BUT, can also decrease performance is working set size cannot fit in cache.
Ultimately, cache performance is measured by the average memory access time (AMAT), which depends cache architecture and size, but also the Access time for hit, miss penalty, hit rate

## Slide 51: Goals for Today: caches
Comparison of cache architectures:
  Direct Mapped
  Fully Associative
  N-way set associative
Caching Questions
  How does a cache work?
  How effective is the cache (hit rate/miss rate)?
  How large is the cache?
  How fast is the cache (AMAT=average memory access time)
Next time: Writing to the Cache
  Write-through vs Write-back
Next time
Notes: Caches vs memory vs tertiary storage
- Tradeoffs: big & slow vs small & fast
- working set: 90/10 rule
- How to predict future: temporal & spacial locality