## Slide 1: CS5412: Using Gossip to Build Overlay Networks
Ken Birman
Lecture XX

## Slide 2: Gossip and Network Overlays
A topic that has received a lot of recent attention
Today we’ll look at three representative approaches
  Scribe, a topic-based pub-sub system that runs on the Pastry DHT (slides by Anne-Marie Kermarrec)
  Sienna, a content-subscription overlay system (slides by Antonio Carzaniga)
  T-Man, a general purpose system for building complex network overlays (slides by Ozalp Babaoglu)

## Slide 3: Scribe
Research done by the Pastry team, at MSR lab in Cambridge England
Basic idea is simple
  Topic-based publish/subscribe
  Use topic as a key into a DHT
    Subscriber registers with the “key owner”
    Publisher routes messages through the DHT owner
  Optimization to share load
    If a subscriber is asked to forward a subscription, it doesn’t do so and instead makes note of the subscription. Later, it will forward copies to its children

## Slide 4: Architecture
TCP/IP
Internet
SCRIBE
Scalable communication
service
Subscription management
Event notification
PASTRY
P2P location and
routing layer
DHT

## Slide 5: Design
Construction of a multicast tree based on the Pastry network
  Reverse path forwarding
  Tree used to disseminate events
Use of Pastry route to create and join groups

## Slide 6: SCRIBE: Tree Management
Create: route to groupId
Join: route to groupId
Tree: union of Pastry routes from members to the root.
Multicast: from the root down to the leaves
Low link stress
Low delay
groupId
join( groupId)
Multicast (groupId)
Root
join( groupId)
Forwards two copies

## Slide 7: SCRIBE: Tree Management
d13da3
65a1fc
d467c4: root
d471f1
Name space
26b20d
Proximity space
26b20d
65a1fc
d13da3
d467c4: root

## Slide 8: Concerns?
Pastry tries to exploit locality but could these links send a message from Ithaca… to Kenya… to Japan…
What if a relay node fails? Subscribers it serves will be cut off
  They refresh subscriptions, but unclear how often this has to happen to ensure that the quality will be good
  (Treat subscriptions as “leases” so that they evaporate if not refreshed… no need to unsubscribe…)

## Slide 9: SCRIBE: Failure Management
Reactive fault tolerance
Tolerate root and nodes failure
Tree repair: local impact
  Fault detection: heartbeat messages
  Local repair

## Slide 10: Scribe: performance
1500 groups, 100,000 nodes, 1msg/group
Low delay penalty
Good partitioning and load balancing
  Number of groups hosted per node : 2.4 (mean) 2 (median)
Reasonable link stress:
  Mean msg/link : 2.4 (0.7 for IP)
  Maximum link stress: 4*IP

## Slide 11: Topic distribution
Group Size
Topic Rank
Instant Messaging
Windows Update
Stock
Alert

## Slide 12: Concern about this data set
Synthetic, may not be terribly realistic
  In fact we know that subscription patterns are usually power-law distributions, so that’s reasonable
  But unlikely that the explanation corresponds to a clean Zipf-like distribution of this nature (indeed, totally implausible)
  Unfortunately, this sort of issue is common when evaluating very big systems using simulations
  Alternative is to deploy and evaluate them in use… but only feasible if you own Google-scale resources!

## Slide 13: Delay penalty
0
250
500
750
1000
1250
1500
0
0.5
1
1.5
2
2.5
3
3.5
4
4.5
Delay Penalty Relative to IP
Cumulative Number of Topics
Mean = 1.66
Median =1.56

## Slide 14: Node stress: 1500 topics
Number of nodes
Total number of children table entries
Mean = 6.2
Median =2

## Slide 15: Scribe Link stress
0
5000
10000
15000
20000
25000
30000
35000
40000
1
10
100
1000
10000
Number of Links
Scribe
IP Multicast
Link stress
Maximum stress
Mean = 1.4
Median = 0

## Slide 16: T-Man
T-Man