## Slide 1: Quiz 1 (on Canvas)
Ends at 1:10pm

## Slide 2: Image Resampling & Interpolation
CS5670: Computer Vision

## Slide 3: Announcements
Project 1 released, due Friday, February 10 by 8pm on GitHub Classroom
  Project to be done solo (teams of one)
  Artifact due Monday, Feb 13 by 8pm

## Slide 4: Image scaling
This image is too big to fit on the screen. How can we generate a half-sized version?
Source: S. Seitz

## Slide 5: Image sub-sampling
Throw away every other row and column to create a 1/2 size image
  - called image sub-sampling
1/4
1/8
Source: S. Seitz

## Slide 6: Image sub-sampling
1/4 (2x zoom)
1/8 (4x zoom)
Why does this look so crufty?
1/2
Source: S. Seitz

## Slide 7: Image sub-sampling – another example
Source: F. Durand

## Slide 8: Even worse for synthetic images
Source: L. Zhang

## Slide 9: Aliasing
Occurs when your sampling rate is not high enough to capture the amount of detail in your image
Can give you the wrong signal/image—an alias
To do sampling right, need to understand the structure of your signal/image
Enter Monsieur Fourier…
  “But what is the Fourier Transform? A visual introduction.” https://www.youtube.com/watch?v=spUNpyF58BY
To avoid aliasing:
  sampling rate ≥ 2 * max frequency in the image
    said another way: ≥ two samples per cycle
  This minimum sampling rate is called the Nyquist rate
Source: L. Zhang

## Slide 10: Wagon-wheel effect
(See http://www.michaelbach.de/ot/mot-wagonWheel/index.html)
Source: L. Zhang

## Slide 11: Wagon-wheel effect
https://en.wikipedia.org/wiki/Wagon-wheel_effect

## Slide 12: Temporal aliasing – helicopter blades
https://www.youtube.com/watch?v=yr3ngmRuGUc

## Slide 13: Aliasing in practice

## Slide 14: Nyquist limit – 2D example
Good sampling
Bad sampling

## Slide 15: Aliasing
When downsampling by a factor of two
  Original image has frequencies that are too high
How can we fix this?

## Slide 16: Gaussian pre-filtering
G 1/4
G 1/8
Gaussian 1/2
Solution: filter the image, then subsample
Source: S. Seitz

## Slide 17: Subsampling with Gaussian pre-filtering
G 1/4
G 1/8
Gaussian 1/2
Solution: filter the image, then subsample
Source: S. Seitz

## Slide 18: Compare with...
1/4 (2x zoom)
1/8 (4x zoom)
1/2
Source: S. Seitz

## Slide 19: Gaussian pre-filtering
Solution: filter the image, then subsample
blur
F0 H
*
subsample
blur
subsample
…
F1
F1 H
*
F2
F0

## Slide 20
blur
F0 H
*
subsample
blur
subsample
…
F1
F1 H
*
F2
F0
{
Gaussian pyramid

## Slide 22: Gaussian pyramids [Burt and Adelson, 1983]
In computer graphics, a mip map [Williams, 1983]
A precursor to wavelet transform
Gaussian Pyramids have all sorts of applications in computer vision
Source: S. Seitz

## Slide 23
How much space does a Gaussian pyramid take compared to the original image?
Source: S. Seitz
Gaussian pyramids [Burt and Adelson, 1983]

## Slide 24: Gaussian pyramid

## Slide 25
How much space (number of pixels) does a Gaussian pyramid of an image take compared to the original image?
ⓘ Start presenting to display the poll results on this slide.

## Slide 26: Gaussian pyramid
Answer: 4/3 the amount of space as the original image alone

## Slide 27: Back to the checkerboard
What should happen when you make the checkerboard smaller and smaller?
Naïve subsampling
Proper prefiltering
(“antialiasing”)
Image turns grey! (Average of black and white squares, because each pixel contains both.)

## Slide 28: Questions?

## Slide 29: Upsampling
This image is too small for this screen:
How can we make it 10 times as big?
Simplest approach:
repeat each row
and column 10 times
(“Nearest neighbor
interpolation”)

## Slide 30: Image interpolation
Recall that a digital images is formed as follows:
  It is a discrete point-sampling of a continuous function
  If we could somehow reconstruct the original function, any new image could be generated, at any resolution and scale
1
2
3
4
5
Adapted from: S. Seitz
d = 1 in this
example

## Slide 31: Image interpolation
1
2
3
4
5
d = 1 in this
example
Recall that a digital images is formed as follows:
  It is a discrete point-sampling of a continuous function
  If we could somehow reconstruct the original function, any new image could be generated, at any resolution and scale
Adapted from: S. Seitz

## Slide 32: Image interpolation
1
2
3
4
5
2.5
1
  Convert to a continuous function:
  Reconstruct by convolution with a reconstruction filter, h
What if we don’t know ?
  Guess an approximation:
  Can be done in a principled way: filtering
d = 1 in this example
Adapted from: S. Seitz

## Slide 33
Image interpolation
“Ideal” reconstruction
Nearest-neighbor interpolation
Linear interpolation
Gaussian reconstruction
Source: B. Curless

## Slide 34: Reconstruction filters
What does the 2D version of this hat function look like?
Often implemented without cross-correlation
  E.g., http://en.wikipedia.org/wiki/Bilinear_interpolation
Better filters give better resampled images
  Bicubic is common choice
performs
linear interpolation
(tent function) performs
bilinear interpolation
Cubic reconstruction filter

## Slide 35
Image interpolation
Nearest-neighbor interpolation
Bilinear interpolation
Bicubic interpolation
Original image: x 10

## Slide 36
Also used for resampling
Image interpolation

## Slide 37: Raster-to-vector graphics

## Slide 38: Depixelating Pixel Art

## Slide 39: Modern methods
From Romano, et al: RAISR: Rapid and Accurate Image Super Resolution, https://arxiv.org/abs/1606.01299

## Slide 40: Super-resolution with multiple images
Can do better upsampling if you have multiple images of the scene taken with small (subpixel) shifts
Some cellphone cameras (like the Google Pixel line) capture a burst of photos
Can we use that burst for upsampling?

## Slide 41: Google Pixel 3 Super Res Zoom
Effect of hand tremor as seen in a cropped burst of photos, after global alignment
https://ai.googleblog.com/2018/10/see-better-and-further-with-super-res.html
Example photo with and without super res zoom (smart burst align and merge)

## Slide 42: Summary
Key points:
  Subsampling an image can cause aliasing. Better is to blur (“pre-filter”) to remote high frequencies then downsample
  If you repeatedly blur and downsample by 2x, you get a Gaussian pyramid
  Upsampling an image requires interpolation. This can be posed as convolution with a “reconstruction kernel”

## Slide 43: Questions?