## Slide 1: Binocular Stereo
CS5670: Computer Vision
Single image stereogram, https://en.wikipedia.org/wiki/Autostereogram
What is this?

## Slide 2: Announcements
Project 3 due this Friday, March 17 at 8pm (code), Monday, March 20 at 8pm (artifact)
Project 4 (Stereo) to be released on Tuesday, March 21, due Friday, April 31, by 8pm
  To be done in groups of two

## Slide 3: From last time: 3D modeling from a photograph
video by Antonio Criminisi

## Slide 4: 3D modeling from a photograph
Flagellation. Piero della Francesca. c1453.

## Slide 5: Related problem: camera calibration
Goal: estimate the camera parameters
  Version 1: solve for 3x4 projection matrix
  Version 2: solve for camera parameters separately
    intrinsics (focal length, principal point, pixel size)
    extrinsics (rotation angles, translation)
    radial distortion

## Slide 6: Vanishing points and projection matrix
= vx (X vanishing point)
Z
3
Y
2
,
similarly,
v
π
v
π
=
=
Not So Fast! We only know v’s up to a scale factor
  Can fully specify by providing 3 reference points with known coordinates

## Slide 7: Calibration using a reference object
Place a known object in the scene
  identify correspondence between image and scene
  compute mapping from scene to image
Issues
  must know geometry very accurately
  must know 3D -> 2D correspondence

## Slide 8: AR codes
ArUco

## Slide 9: Estimating the projection matrix
Place a known object in the scene
  identify correspondence between image and scene
  compute mapping from scene to image

## Slide 10: Alternative: multi-plane calibration
Images courtesy Jean-Yves Bouguet
Advantage
  Only requires a plane
  Don’t have to know positions/orientations
  Good code available online! (including in OpenCV)
    Matlab version by Jean-Yves Bouget: http://www.vision.caltech.edu/bouguetj/calib_doc/index.html
    Amy Tabb’s camera calibration software: https://github.com/amy-tabb/basic-camera-calibration

## Slide 11: Single-image depth prediction using deep learning
Image
Depth map
Deep learning
Li and Snavely. Megadepth: Learning single-view depth prediction from internet photos. CVPR 2018.

## Slide 12: MiDaS depth prediction
https://github.com/intel-isl/MiDaS
https://gradio.app/g/AK391/MiDaS
Ranftl et al. Towards Robust Monocular Depth Estimation: Mixing Datasets for Zero-shot Cross-dataset Transfer.

## Slide 13: Single-image depth prediction
Picture credit: Magritte, The Treachery of Images, and the Berkeley Computer Vision Group
Miangoleh*, Dille*, Mai, Paris, and Aksoy.
Boosting Monocular Depth Estimation Models to High-Resolution via Content-Adaptive Multi-Resolution Merging.
CVPR 2021.
Notes: So where to go from here? I think there are a lot of very interesting open directions. Of all of these Im2Scene tasks, single-view depth prediction is one of the most mature.
Beautiful ambiguity of perception.
Yağız Aksoy, SFU

## Slide 14: Deep geometry prediction
More on this topic later!

## Slide 15: Questions?

## Slide 16
“Mark Twain at Pool Table", no date, UCR Museum of Photography

## Slide 17
https://giphy.com/gifs/wigglegram-706pNfSKyaDug

## Slide 18: Stereo Vision as Localizing Points in 3D
An object point will project to some point in our image
That image point corresponds to a ray in the world
Two rays intersect at a single point, so if we want to localize points in 3D we need 2 eyes

## Slide 19: Stereo
Given two images from different viewpoints
  How can we compute the depth of each point in the image?
  Based on how much each pixel moves between the two images

## Slide 20: Epipolar geometry
epipolar lines
(x1, y1)
(x2, y1)
x2 - x1 = the disparity of pixel (x1, y1)
Two images captured by a purely horizontal translating camera
(rectified stereo pair)

## Slide 21: Disparity = inverse depth
http://stereo.nypl.org/view/41729
(Or, hold a finger in front of your face and wink each eye in succession.)

## Slide 22: Your basic stereo matching algorithm
Match Pixels in Conjugate Epipolar Lines
  Assume brightness constancy
  This is a challenging problem
  Hundreds of approaches
    A good survey and evaluation: http://www.middlebury.edu/stereo/

## Slide 23: Your basic stereo matching algorithm
For each epipolar line
For each pixel in the left image
    compare with every pixel on same epipolar line in right image
    pick pixel with minimum match cost
Improvement: match windows

## Slide 24: Stereo matching based on SSD
SSD
dmin d
Best matching disparity

## Slide 25: Window size
  Smaller window
    more detail
    - more noise
  Larger window
    less noise
    - less detail
W = 3
W = 20
Better results with adaptive window
  T. Kanade and M. Okutomi, A Stereo Matching Algorithm with an Adaptive Window: Theory and Experiment, ICRA 1991.
  D. Scharstein and R. Szeliski. Stereo matching with nonlinear diffusion. IJCV, July 1998
Effect of window size
Notes: smaller window: more detail, more noise
bigger window: less noise, more detail

## Slide 26: Stereo results
  Data from University of Tsukuba
  Similar results on other images without ground truth
Ground truth
Scene

## Slide 27: Results with window search
Window-based matching
(best window size)
Ground truth

## Slide 28: Better methods exist...
Graph cuts-based method
  Boykov et al., Fast Approximate Energy Minimization via Graph Cuts,
  International Conference on Computer Vision 1999.
Ground truth
    For the latest and greatest: http://www.middlebury.edu/stereo/

## Slide 29: Stereo as energy minimization
What defines a good stereo correspondence?
  Match quality
    Want each pixel to find a good match in the other image
  Smoothness
    If two pixels are adjacent, they should (usually) move about the same amount

## Slide 30: Stereo as energy minimization
Find disparity map d that minimizes an energy function
Simple pixel / window matching
SSD distance between windows I(x, y) and J(x + d(x,y), y)
=

## Slide 31: Stereo as energy minimization
y = 141
C(x, y, d); the disparity space image (DSI)
x
d

## Slide 32: Stereo as energy minimization
y = 141
x
d
Simple pixel / window matching: choose the minimum of each column in the DSI independently:

## Slide 33: Greedy selection of best match

## Slide 34: Stereo as energy minimization
Better objective function
{
{
match cost
smoothness cost
    Want each pixel to find a good match in the other image
    Adjacent pixels should (usually) move about the same amount

## Slide 35: Stereo as energy minimization
match cost:
smoothness cost:
4-connected neighborhood
8-connected neighborhood
: set of neighboring pixels

## Slide 36: Smoothness cost
“Potts model”
L1 distance
How do we choose V?

## Slide 37: Smoothness cost
If λ = infinity, then we only consider smoothness
Optimal solution is a surface of constant depth/disparity
  Fronto-parallel surface
In practice, want to balance data term with smoothness term

## Slide 38: Dynamic programming
Can minimize this independently per scanline using dynamic programming (DP)

## Slide 39: Dynamic programming
Finds “smooth”, low-cost path through DPI from left to right
Visiting a node incurs its data cost, switching disparities from one column to the next also incurs a (smoothness) cost
y = 141
x
d

## Slide 40: Dynamic Programming

## Slide 41: Dynamic programming
Can we apply this trick in 2D as well?
No: the shortest path trick only works to find a 1D path
Slide credit: D. Huttenlocher

## Slide 42: Stereo as a minimization problem
The 2D problem has many local minima
  Gradient descent doesn’t work well
And a large search space
  n x m image w/ k disparities has knm possible solutions
  Finding the global minimum is NP-hard in general
Good approximations exist (e.g., graph cuts algorithms)

## Slide 43: Questions?

## Slide 44: Depth from disparity
f
x
x’
baseline
z
C
C’
X
f

## Slide 45: Stereo reconstruction pipeline
  Camera calibration errors
  Poor image resolution
  Occlusions
  Violations of brightness constancy (specular reflections)
  Large motions
  Low-contrast image regions
Steps
  Calibrate cameras
  Rectify images
  Compute disparity
  Estimate depth
What will cause errors?

## Slide 46: Variants of stereo

## Slide 47: Real-time stereo
Used for robot navigation (and other tasks)
  Several real-time stereo techniques have been developed (most based on simple discrete search)
Nomad robot searches for meteorites in Antartica

## Slide 48: Active stereo with structured light
Project “structured” light patterns onto the object
  simplifies the correspondence problem
  basis for active depth sensors, such as Kinect and iPhone X (using IR)
camera 2
camera 1
projector
camera 1
projector
Li Zhang’s one-shot stereo

## Slide 49: Active stereo with structured light
https://ios.gadgethacks.com/news/watch-iphone-xs-30k-ir-dots-scan-your-face-0180944/

## Slide 50: Laser scanning
Optical triangulation
  Project a single stripe of laser light
  Scan it across the surface of the object
  This is a very precise version of structured light scanning
Digital Michelangelo Project
http://graphics.stanford.edu/projects/mich/

## Slide 51: Laser scanned models
  The Digital Michelangelo Project, Levoy et al.

## Slide 52: Laser scanned models
  The Digital Michelangelo Project, Levoy et al.

## Slide 53: Laser scanned models
  The Digital Michelangelo Project, Levoy et al.

## Slide 54: Laser scanned models
  The Digital Michelangelo Project, Levoy et al.

## Slide 55: 3D Photography on your Desk
http://www.vision.caltech.edu/bouguetj/ICCV98/

## Slide 56: Questions?